## Slide 1: Investigating time series neural data: Experimental design & processing

## Slide 2: Experiment Description
TMSI Refa8 EEG amplifier
  Sampling rate: 256 Hz
  17 electrode: fronto-central, central, centro-parietal, and parietal
OpenVIBE software
  EEG recording
  display of visual cues
  Feedback
  Online classification

## Slide 3: Participants and tasks
Sixteen naive participants
  13 males and three females
  mean age = 28 ± 9 years
Tasks
  cued motor imagery
  left hand, right hand, left foot, and right foot
  Each session
    24 trials for each motor imagery task
Visual or somatosensory feedback

## Slide 4: Recorded EEG signal analysis
5s epoched from 1s before feedback onset
Bandpass filtered [0.5, 40] Hz
re-referenced at Fz
common spatial patterns (CSPs) to extract the feature vectors
linear discriminant analysis (LDA) classifier

## Slide 5: Exercises
Temporal filter: Apply a low-pass filter of your choice with a cut-off at
  6 Hz
  32 Hz
Spatial filter: Apply a Laplacian filter for electrodes
  FCz, Cz and CPz
Baseline correct the
  temporally filtered data
  spatially filtered data
Plot the grand averages of the electrodes: Cz, FCz and CPz for the time range [1.5, 3] s
Plot and analyse the time-frequency distribution of the signals using Morlet Wavelet
  temporally filtered data
  spatially filtered data